## Slide 1
MRS BEARINGS PRIVATE LIMITED
PRODUCTION | UNIT
March
2026
Performance Report
PERIOD March 1 – 31, 2026
PREPARED BY Production Management Team
Operational & KPI Review
COMPANY
MRS Bearings Private Limited
DEPARTMENT
Production
REPORTING PERIOD
March 1 – 31 , 2026
PREPARED BY
Production Management Team
CONFIDENTIAL | FOR MANAGEMENT REVIEW | MRS BEARINGS PRIVATE LIMITED

## Slide 2
BELOW TARGET
Process Capability (Cpk)
1.59
Target: ≥ 1.67
BELOW TARGET
Production Achievement
86%
Target: >95%
CRITICAL
IG Rejection (ppm)
11,113
Target: <1,500 ppm
7× OVER TARGET
CRITICAL
IG Rework (ppm)
27,609
Target: <7,500 ppm
3× OVER TARGET
ON TARGET
Average Output per person Production
7,467
Target: >5000
BELOW TARGET
OEE – IG Machines Avg.
58 %
Target: >65%
Key Insight
IG section requires immediate attention with 14× rejection and 5× rework over targets.
Key Performance Indicators – March 2026

## Slide 3
Process Capability (Cpk) – March 2026
Machine | 01-Mar | 06-Mar | 08-Mar | 09-Mar | 15-Mar | 17-Mar | 18-Mar | 19-Mar | 20-Mar | 22-Mar | Average
IG.01 |  | 2.45 |  |  |  | 0.95 | 2.15 |  |  |  | 1.85
IG.04 | 1.50 |  |  | 0.85 |  | 1.03 |  | 2.11 |  |  | 1.37
IG.11 |  |  |  |  |  |  |  |  |  |  | -
IG.12 | 1.10 |  |  |  |  |  | 0.70 |  | 1.68 |  | 1.16
IG.13 |  |  |  |  |  |  |  |  |  |  | -
IG.14 |  |  |  |  |  |  |  |  |  |  | -
IG.15 |  |  |  | 1.18 | 1.31 |  |  |  |  | 1.34 | 1.28
IG.16 |  |  | 1.72 |  |  |  |  |  |  |  | 1.72
IG.17 |  |  |  |  |  |  |  |  |  | 1.91 | 1.91
IG.18 | 1.81 |  |  |  |  |  |  |  |  |  | 1.81
Cpk ≥ 1.33 (Good)
1.00 ≤ Cpk < 1.33 (Monitor)
Cpk < 1.00 (Action Needed)
Fleet Average: 1.59 Cpk (Target: ≥ 1.67) | Best: IG.17 at 1.91 | Danger Zone: IG.12 at 1.16 needs monitoring
CONFIDENTIAL | FOR MANAGEMENT REVIEW | MRS BEARINGS PRIVATE LIMITED
Process Capability (Cpk)

## Slide 4: Production Achievement – IG Machines
Plan vs Good Qty
IG.01
IG.04
IG.11
IG.12
IG.13
IG.14
IG.17
IG.18
IG.19
IG.20
0
10000
20000
30000
40000
50000
60000
70000
Plan Qty
Good Qty
IG Fleet Summary
Total Planned (Target)
4,43,200
Total Rework
8,329
Total Loss Qty
91,564
Achievement %
68%
Efficiency Loss %
11%
Downtime (hrs)
1393 (21%)
Total Rejection
3,416
Sum of Good
2,98,904
Sum of Total
3,03,082
64513
53861
38000
26029
16354
7833
34716
20049
20233
10299
60137
45115
37749
51856
37417
39558
19612
46800
30141
5918
2072
6586
15020
IG.16
IG.15
51537

## Slide 5: IG Section – Downtime Analysis (Minutes)
March 2026 | Total: 1,393 hrs | 12 M/C
Machine | Re-Setting | Ovality | Taper | Size Var. | Dia Turn | Dia Chg | Tool Wait | No Oper. | No Power | Mech Mnt | Elec Mnt | Other | Total Hrs
IG.01 | 175 | - | - | 280 | 30 | 5 | 180 | 2030 | 820 | - | - | 85 | 69
IG.04 | 290 | - | 485 | 210 | 65 | 55 | - | 3045 | 860 | 150 | 240 | 200 | 124
IG.12 | 245 | - | 385 | 600 | 175 | 10 | - | 3970 | 845 | 80 | - | 120 | 154
IG.13 | 690 | 655 | 750 | 80 | 30 | 30 | 30 | 6585 | 805 | - | 20 | 165 | 176
IG.14 | 170 | 35 | 85 | 20 | - | - | - | 2135 | 820 | - | - | 35 | 69
IG.15 | 95 | 60 | 425 | 370 | 220 | 20 | - | 540 | 930 | - | - | 235 | 57
IG.16 | 250 | 75 | 505 | 210 | 160 | 20 | - | 230 | 925 | 55 | 20 | 350 | 59
IG.17 | 155 | - | 355 | 535 | 185 | 15 | 180 | 6500 | 805 | 15 | 10 | 225 | 158
IG.18 | 1210 | 230 | 190 | 320 | 155 | 10 | - | 2960 | 895 | 240 | 85 | 230 | 131
No Operator is the #1 downtime factor
IG.13 (6,585 min) & IG.17 (6,500 min) have the highest No Operator time. IG.12 (3,970 min) and IG.04 (3,045 min) also critical. IG.18 has the highest Re-Setting time at 1,210 min — needs process optimization.

## Slide 6: Production Achievement – EG Machines
March 2026 | Good Output by Machine
EG.02
EG.04
EG.05
EG.07
EG.08
0
5000
15000
10000
25000
20000
30000
35000
40000
45000
29,648
2,610
15,588
39,723
6,069
EG Fleet Summary
Total Good | 93,638
Total Rework | 440
Total Rejection | 344
Rework PPM | 5,537
Rejection PPM | 3,697

## Slide 7: EG Section – Production Summary
March 2026
Machine | Plan Qty Good Qty | Rework | T . Rej Rejection | Total
EG.02 | 29,648 | 66 | 49 | 29,700
EG.04 | 2,610 | 180 | 65 | 2,681
EG.05 | 15,588 | 80 | 195 | 15,785
EG.07 | 39,723 | 91 | 17 | 39,740
EG.08 | 6,069 | 23 | 18 | 6,088
Grand Total | 93,638 | 440 | 344 | 93,994
EG PPM Analysis
Rework PPM: 5,537 (Target: <3,000) — ABOVE TARGET Rejection PPM: 3,697 (Target: <1,500) — ABOVE TARGET
EG.04 has highest rework (180 pcs) — needs attention
Key Observations
EG.07 is the best performer — 39,723 good with only 91 rework EG.05 has highest rejection (195 pcs) — root cause needed EG.04 lowest output (2,610) with highest rework rate
44977
10848
27105
62985
10720
156635
3
6
2
0
1
195

## Slide 8: EG Section – Rework Analysis (Machine-wise)
March 2026
EG.04
EG.07
EG.05
EG.02
EG.08
200
180
160
140
120
100
80
60
40
20
0
180
91
80
66
23
EG Rework Summary
Total EG Rework: 440 pcs
Rework PPM: 5,537 (Target: <3,000)
EG.04: 180 pcs — Highest rework, lowest output (2,610 good). Rework rate is extremely high.
EG.07: 91 pcs — Good volume (39,723) keeps PPM manageable. EG.08: 23 pcs — Best rework control.

## Slide 9: EG Section – Rejection Analysis (Machine-wise)
March 2026
EG.05
EG.04
EG.02
EG.08
EG.07
0
50
100
150
200
250
195
65
49
18
17
EG Rejection Summary
Total EG Rejection: 344 pcs
Rejection PPM: 3,697 (Target: <1,500)
EG.05: 195 pcs — Highest rejection count. Root cause analysis needed. EG.04: 65 pcs — High relative to low output.
EG.07: 17 pcs — Best performer in rejection control.

## Slide 10: Production Achievement – HO Machines
March 2026 | Good Output by Machine
HO.02
HO.03
HO.06
HO.07 IR
HO.07 OR
HO.08 IR
HO.08 OR
HO.09 IR
HO.09 OR
HO.10
0
20000
30000
40000
50000
60000
70000
10, 639
10000
20, 845
21, 793
53, 485
19, 113
18, 357
62, 921
38, 043
40, 690
4,747
HO Fleet Summary
Total Good
290,633
Total Rework
54
Total Rejection
44
Near-Zero Defects
Excellent

## Slide 11: HO Section – Production Summary
March 2026 | Near-Zero Defects Performance
Machine | Good Qty | Rework | Rejection | Total
HO.02 | 10,639 | 0 | 0 | 10,639
HO.03 | 20,845 | 0 | 0 | 20,846
HO.06 | 21,793 | 0 | 0 | 21,793
HO.07 IR | 53,485 | 0 | 5 | 53,490
HO.07 OR | 19,113 | 54 | 15 | 19,128
HO.08 IR | 18,357 | 0 | 0 | 18,357
HO.08 OR | 62,921 | 0 | 24 | 62,954
HO.09 IR | 38,043 | 0 | 0 | 38,043
HO.09 OR | 40,690 | 0 | 0 | 40,695
HO.10 | 4,747 | 0 | 0 | 4,747
Grand Total | 290,633 | 54 | 44 | 290,692
HO Section: Outstanding quality performance — Near-zero rework (54 pcs) and rejection (44 pcs) across 290,633 good output.

## Slide 12: HO Section – Rework Analysis (Machine-wise)
March 2026
HO.07 OR
HO.02
HO.03
HO.06
0
10
20
30
50
40
60
54
0
0
0
0 0 0 0 0 0
HO.07 IR HO.08 IR HO.08 OR HO.09 IR HO.09 OR HO.10
HO Rework Summary
Total Rework: 54 pcs (Only HO.07 OR)
HO.07 OR: 54 pcs rework out of 19,113 good
All other HO machines: ZERO rework
Excellent quality control across HO section

## Slide 13: HO Section – Rejection Analysis (Machine-wise)
March 2026
HO.08 OR HO.07 OR HO.07 IR HO.02
HO.03
HO.06
0
5
10
15
20
25
30
24
15
5
0
0
0
0 0 0 0
HO.08 IR HO.09 IR HO.09 OR HO.10
HO Rejection Summary
Total Rejection: 44 pcs
HO.08 OR: 24 pcs (highest) HO.07 OR: 15 pcs
HO.07 IR: 5 pcs
7 out of 10 machines: ZERO rejection

## Slide 14: IG Section – Rework Analysis (Machine-wise)
March 2026 | PPM = (Rework ÷ Good) × 1,000,000
Machine | Good Qty | Rework Qty | Rework PPM | Observation
IG.15 | 37,749 | 1,147 | 30,384 | Action Needed
IG.12 | 20,049 | 1,146 | 57,160 | Action Needed
IG.13 | 10,299 | 1,070 | 103,894 | Action Needed
IG.14 | 45,115 | 969 | 21,478 | Monitor
IG.17 | 19,612 | 847 | 43,189 | Monitor
IG.04 | 26,029 | 581 | 22,323 | Monitor
IG.16 | 39,558 | 574 | 14,512 | Monitor
IG.18 | 30,141 | 510 | 16,919 | Monitor
IG.11 | 7,833 | 472 | 60,259 | OK
IG.19 | 2,072 | 424 | 204,633 | OK
IG.01 | 53,861 | 423 | 7,853 | OK
IG.20 | 6,586 | 166 | 25,197 | OK
Grand Total | 298,904 | 8,329 | 27,609 | 3.7× over target

## Slide 15: Operator Performance – IG Machines
March 2026 | Top Performers by Good Output
Machine | Top 1 (Good Qty) | Top 2 (Good Qty) | Top 3 (Good Qty)
IG.01 | Hritik Singh — 16,719 | Akash Kumar — 14,001 | Taslimbhai Kondhiya — 8,833
IG.04 | Raymalbhai Bharathiya — 8,960 | Rutvik — 6,632 | Akash Kumar — 5,434
IG.11 | Shamjibhai Satapara — 1,442 | Ramesh Shakriya — 1,217 | Akshay — 1,070
IG.12 | Anand P — 4,859 | Vishal D — 2,273 | Ramesh Shakriya — 2,107
IG.13 | Shamjibhai Satapara — 4,356 | Dilip Panday — 3,068 | Amit Makampara — 1,237
IG.14 | Kaushik Vasveliya — 17,718 | Abhijitsinh Rana — 13,495 | Vala Himesh — 5,965
IG.15 | Dilip Panday — 7,898 | Hashmukh — 7,525 | Vala Himesh — 3,971
IG.16 | Shrawan Matho — 19,641 | Pravin Baraiya — 7,886 | Shamjibhai Satapara — 3,090
IG.17 | Varshaben Mankoliya — 5,927 | Hashmukh — 2,998 | Dilip Panday — 2,463
IG.18 | Ramesh Shakriya — 3,874 | Hashmukh — 3,393 | Taslimbhai Kondhiya — 3,135
IG.19 | Rinaben Oganiya — 1,025 | Kiran Vaghadiya — 574 | Pankajbhai Khasiya — 278
IG.20 | Kiran Vaghadiya — 4,915 | Varshaben Mankoliya — 939 | Pawan — 504

## Slide 16: Operator Performance – HO Machines
March 2026 | Top Performers by Good Output
Machine | Top 1 (Good Qty) | Top 2 (Good Qty) | Top 3 (Good Qty)
HO.02 | Rinaben Oganiya — 4,911 | Ramdev — 1,418 | Sunil — 1,285
HO.03 | Parulben Ranga — 17,204 | Nihar Sheth — 1,163 | Pravin Baraiya — 1,050
HO.06 | Parulben Ranga — 10,001 | Navghan — 4,670 | Nihar Sheth — 2,094
HO.07 IR | Ravikumar Sharma — 14,974 | Ramdev — 14,061 | Navghan — 3,150
HO.07 OR | Ravikumar Sharma — 4,127 | Nihar Sheth — 2,924 | Mehul M — 2,585
HO.08 IR | Nihar Sheth — 5,733 | Ravikumar Sharma — 2,166 | Pankaj Oganiya — 2,144
HO.08 OR | Ravikumar Sharma — 9,097 | Nihar Sheth — 8,052 | Navghan — 7,766
HO.09 IR | Pankaj Oganiya — 11,916 | Mehul M — 7,408 | Nihar Sheth — 4,871
HO.09 OR | Pankaj Oganiya — 10,463 | Nihar Sheth — 5,403 | Mehul M — 5,381
HO.10 | Varshaben Mankoliya — 2,190 | Mehul M — 1,055 | Ravikumar Sharma — 917

## Slide 17: Operator Performance – EG Machines
March 2026 | Top Performers by Good Output
Machine | Top 1 (Good Qty) | Top 2 (Good Qty) | Top 3 (Good Qty)
EG.02 | Pawan — 12,759 | Jaglal Gupta — 11,739 | Rinaben Oganiya — 2,496
EG.04 | Dilip Panday — 600 | Pawan — 567 | Abhijitsinh Rana — 361
EG.05 | Kiran Vaghadiya — 7,468 | Rinaben Oganiya — 3,140 | Jaglal Gupta — 2,211
EG.07 | Kiran Vaghadiya — 6,052 | Pawan — 5,530 | Rinaben Oganiya — 4,469
EG.08 | Kiran Vaghadiya — 2,199 | Jaglal Gupta — 1,749 | Pawan — 804
Key Performer Insights
Kiran Vaghadiya leads across EG.05, EG.07, EG.08 — consistent high performer. Pawan contributes significantly across EG.02, EG.04, EG.07 — versatile operator. Jaglal Gupta strong on EG.02 (11,739) and EG.08 (1,749).

## Slide 18: Overall Equipment Effectiveness (OEE) March 2026 | Target: >65%
Fleet OEE
58%
Target: >65%
IG.01
IG.04
IG.11
IG.12
IG.13
IG.14
IG.15
IG.16
IG.17
IG.18
IG.19
IG.20
0
10
20
30
40
50
60
70
80
90
84
69
48
58
49
75
73
76
52
64
35
44
Key Highlights
Best: IG.01 (83.5%)
IG.16 (76.3%), IG.14 (75%)
Worst: IG.19 (35%)
IG.20 (43.9%), IG.11 (47.9%)

## Slide 19: Machine-wise OEE – IG Section
March 2026 | Detailed Breakdown
Machine | Plan Qty | Good Qty | Downtime (hrs) | Achievement % | OEE % | Status
IG.01 | 64,513 | 53,861 | 69 | 83.5% | 83.5% | Above Target
IG.04 | 38,000 | 26,029 | 124 | 68.5% | 68.5% | Above Target
IG.11 | 16,354 | 7,833 | 181 | 47.9% | 47.9% | Critical
IG.12 | 34,716 | 20,049 | 154 | 57.8% | 57.8% | Below Target
IG.13 | 20,933 | 10,299 | 176 | 49.2% | 49.2% | Critical
IG.14 | 60,137 | 45,115 | 87 | 75.0% | 75.0% | Above Target
IG.15 | 51,537 | 37,749 | 57 | 73.3% | 73.3% | Above Target
IG.16 | 51,856 | 39,558 | 59 | 76.3% | 76.3% | Above Target
IG.17 | 37,417 | 19,612 | 158 | 52.4% | 52.4% | Below Target
IG.18 | 46,800 | 30,141 | 131 | 64.4% | 64.4% | Below Target
IG.19 | 5,918 | 2,072 | 108 | 35.0% | 35.0% | Critical
IG.20 | 15,020 | 6,586 | 88 | 43.9% | 43.9% | Critical
Fleet Avg | 443,200 | 298,904 | 1,393 | 67.4% | 58% | Below Target

## Slide 20: Machine-wise OEE – HO Section
March 2026 | Near-Zero Defect Performance
HO.02
HO.03
HO.06
HO.07 IR
HO.07 OR
HO.08 IR
HO.08 OR
HO.09 IR
HO.09 OR
HO.10
40
30
20
10
0
50
60
70
80
62
68
65
72
58
60
75
70
72
45
HO Section Average OEE: ~65% | Best: HO.08 OR (75%) | Quality Rate: Near 100% across all machines

## Slide 21: Machine-wise OEE – EG Section
March 2026
EG.02
EG.04
EG.05
EG.07
EG.08
0
10
20
30
40
50
60
70
80
65
35
55
72
48
EG OEE Summary
Fleet Average: ~55%
Target: >65%
Best: EG.07 (72%)
Highest output with lowest defects.
Worst: EG.04 (35%)
Lowest output, highest rework rate.
EG.08 (48%) needs improvement.