## Slide 1
MRS BEARINGS PRIVATE LIMITED
PRODUCTION | UNIT
FEB
2026
Performance Report
PERIOD February 1 – 28, 2026
PREPARED BY Production Management Team
Operational & KPI Review
COMPANY
MRS Bearings Private Limited
DEPARTMENT
Production
REPORTING PERIOD
February 1 – 28, 2026
PREPARED BY
Production Management Team
CONFIDENTIAL | FOR MANAGEMENT REVIEW | MRS BEARINGS PRIVATE LIMITED

## Slide 2
Key Performance Indicators – February 2026
BELOW TARGET
Process Capability (Cpk)
1.35
Target: ≥ 1.67
BELOW TARGET
Production Achievement
69%
Target: >95%
CRITICAL
IG Rejection (ppm)
18,747
Target: <1,500 ppm
14× OVER TARGET
CRITICAL
IG Rework (ppm)
32,343
Target: <7,500 ppm
5× OVER TARGET
ON TARGET
Average Output per person Production
7626
Target: >5000
BELOW TARGET
OEE – IG Machines Avg.
56.1%
Target: >65%
Key Insight
IG section requires immediate attention with 14× rejection and 5× rework over targets.
Key Performance Indicators – February 2026

## Slide 3
Process Capability (Cpk)
Machine | 02 Feb | 03 Feb | 04 Feb | 05 Feb | 07 Feb | 08 Feb | 13 Feb | 14 Feb | 15 Feb | 16 Feb | 17 Feb | 24 Feb | 28 Feb | Average
IG.01 |  |  |  |  |  |  |  |  | 1.59 |  |  |  | 1.53 | 1.56
IG.04 |  |  |  | 1.17 |  |  |  | 0.99 |  |  |  |  |  | 1.08
IG.11 |  | 1.15 | 2.29 |  | 1.2 |  |  |  |  | 1.16 |  |  |  | 1.45
IG.12 |  |  |  |  |  |  | 0.42 |  |  |  |  |  |  | 0.42
IG.13 |  |  |  |  |  |  |  |  |  |  |  |  |  | #DIV/0!
IG.14 |  |  |  |  |  |  |  |  |  |  |  |  |  | #DIV/0!
IG.15 | 1.24 |  |  |  | 1.18 |  |  |  |  |  | 1.43 | 1.11 |  | 1.24
IG.16 |  |  |  |  |  | 1.01 |  |  |  |  | 1.51 |  |  | 1.26
IG.17 |  |  |  | 1.02 |  |  |  |  |  |  | 1.13 |  |  | 1.075
IG.18 |  | 1.52 |  |  |  | 1.26 |  |  |  |  | 1.2 |  |  | 1.327
Cpk ≥ 1.33 (Good)
1.00 ≤ Cpk < 1.33 (Monitor)
Cpk < 1.00 (Action Needed)
Best Performer: IG.01 at 1.56 shows
Fleet Average: 1.35 Cpk (Target: ≥ 1.67).
the most stable process.
Danger Zone: IG.12 at 0.42 Cpk is critically unstable and needs calibration.

## Slide 4
Production Achievement
Chart: 
| IG.14 | IG.01 | IG.16 | IG.15 | IG.18 | IG.04 | IG.11 | IG.20 | IG.13 | IG.12 | IG.17 | IG.19
Plan Qty | 62622 | 60997 | 52484 | 50667 | 38763 | 37097 | 32035 | 28290 | 25877 | 21474 | 13697 | 5520
Good Qty | 49901 | 48836 | 42431 | 33484 | 23871 | 21625 | 15504 | 12059 | 13808 | 13855 | 5716 | 2641
IG Fleet Summary
Total Planned (Target)
429,523
Total Rework
9,455
Total Loss Qty
86,147
Achievement %
68%
Efficiency Loss %
(52750) 12%
Downtime (hrs)
(1,766) 20%
Total Rejection
5,440
Sum of Good
283731
Sum of Total
290,626

## Slide 5
IG Section – Downtime Analysis
IG.19
367 hrs
No Operator
191h
Not In Plan
96h
Top: 52% from "No Operator"
IG.17
332 hrs
No Operator
179h
Mech Maint
56h
Top: 54% from "No Operator"
IG.20
302 hrs
No Operator
180h
Not In Plan
72h
Top: 59% from "No Operator"
IG.11
261 hrs
No Operator
165h
Not In Plan
40h
Top: 63% from "No Operator"
IG.12
261 hrs
Not In Plan
144h
No Operator
66h
Top: 55% from "Not In Plan"
IG.13
192 hrs
No Operator
96h
New Setting
26h
Top: 50% from "No Operator"
IG.18
180 hrs
No Operator
124h
New Setting
14h
Top: 69% from "No Operator"
IG.04
134 hrs
Wheel Change
23h
No Operator
20h
Top: 17% from "Wheel Change"
IG.14
115 hrs
No Material (Ext)
40h
Wheel Change
22h
Top: 35% from "No Material (Ext)"
IG.01
115 hrs
No Material (Ext)
32h
No Operator
22h
Top: 28% from "No Material (Ext)"
IG.15
101 hrs
No Operator
25h
New Setting
19h
Top: 24% from "No Operator"
IG.16
69 hrs
Wheel Change
14h
New Setting
12h
Top: 20% from "Wheel Change"
Total: 2,510 | 12 M/C
>250 hrs — Critical
150–250 hrs — High
80–150 hrs — Medium
<80 hrs — Low
Critical Machines (>250 hrs Downtime)
IG.19 (367 hrs): Highest downtime; majorly due to No Operator (191h) and Not In Plan (96h).
IG.17 (332 hrs): Driven by No Operator (179h) and Mechanical Maintenance (56h) issues.
IG.20 (302 hrs): Primarily affected by No Operator (180h) and Not In Plan (72h) gaps.
IG.11 (261 hrs): Main losses from No Operator (165h) and Not In Plan (40h).
IG.12 (261 hrs): Primary issue is Not In Plan (144h), followed by No Operator (66h)

## Slide 6
Medium & Low Downtime Machines (<150 hrs)
IG.04 (134 hrs): High Wheel Change time and No Operator issues.
IG.14 (115 hrs): Impacted by External Material Shortage and Wheel Change delays.
IG.01 (115 hrs): Primarily affected by External Material Shortage.
IG.15 (101 hrs): Issues with No Operator and New Setting times.
IG.16 (69 hrs): Technical delays due to Wheel Change and New Settings.
IG Section – Downtime Analysis
Total: 2,510 | 12 M/C
Final Analysis: Root Causes
Labor Shortage (No Operator): Biggest bottleneck; machines sitting idle due to staff unavailability.
Planning Gaps (Not In Plan): Capacity waste; machines ready but excluded from production schedule.
Process Delays (Wheel Change / New Setting): Excessive setup times slowing down production flow.
High Downtime Machines
(150–250 hrs)
IG.13 (192 hrs): Mainly due to No Operator (96h) and delays in New Setting (26h).
IG.18 (180 hrs): Dominant issue is No Operator (124h) , followed by New Setting (14h).

## Slide 7
IG Section — Complete Downtime Detail (hours) | Feb 2026
Reason ↓ M/c →
IG.19
IG.17
IG.20
IG.11
IG.12
IG.13
IG.18
IG.04
IG.14
IG.01
IG.15
IG.16
No Operator
191.3
179.2
179.6
164.8
65.5
95.7
123.5
19.6
7.7
21.9
24.8
11.7
Not In Plan
96.0
56.0
72.0
40.0
144.0
16.2
-
-
-
-
-
-
No Material (Ext)
56.0
-
24.0
-
24.0
-
-
8.0
40.0
32.0
-
8.0
Wheel Change
2.5
13.9
4.2
9.7
7.4
11.3
11.3
23.2
21.7
12.2
18.0
13.8
New Setting
-
9.6
-
14.7
8.5
26.2
13.9
18.5
19.8
10.2
18.8
12.0
Re-Setting
1.9
3.6
11.4
7.5
-
9.9
9.0
15.8
2.8
13.8
9.7
5.3
Taper
-
2.9
0.8
3.9
3.2
5.4
4.4
12.3
-
-
4.6
2.1
Ovality
-
-
-
-
2.0
11.0
1.2
6.5
-
-
2.3
-
Step Problem
-
-
-
-
-
8.2
-
-
-
-
-
-
Mech Maint
-
56.2
-
2.8
-
-
-
-
-
2.0
-
-
Elec Maint
12.6
-
1.6
-
-
-
-
-
2.4
-
-
-
No Power
2.4
4.1
3.1
3.1
2.6
4.4
4.8
4.2
4.5
3.3
6.1
5.7
Size Variation
-
2.6
-
11.8
1.9
3.6
5.2
-
-
-
5.5
2.2
TOTAL
367
332
302
261
261
192
180
134
115
115
101
69
Red = >100 hrs | Orange = >50 hrs | IG.19 & IG.20 worst in No Operator | IG.12 & IG.17 high in Not In Plan

## Slide 8
M/c2 | Sum of M/C Plan Qty. | Sum of Good | Sum of Rework | Sum of IN Running REJ. | Sum of Total | Sum of Down Time (Hrs) | Sum of Total Loss Qty.
IG.01 | 60,997 | 48,836 | 649 | 1,299 | 50,253 | 100 | 8,497
IG.04 | 37,097 | 21,625 | 1,135 | 602 | 22,252 | 104 | 8,727
IG.12 | 21,474 | 13,855 | 704 | 214 | 14,079 | 107 | 3,822
IG.13 | 25,877 | 13,808 | 930 | 257 | 14,064 | 142 | 7,521
IG.14 | 62,622 | 49,901 | 693 | 213 | 50,249 | 74 | 5,748
IG.15 | 50,667 | 33,484 | 2,055 | 800 | 35,407 | 66 | 7,215
IG.16 | 52,484 | 42,431 | 277 | 323 | 42,761 | 46 | 4,739
IG.17 | 13,697 | 5,716 | 538 | 188 | 5,907 | 263 | 4,566
IG.18 | 38,763 | 23,871 | 899 | 730 | 24,613 | 159 | 10,443
IG.11 | 32,035 | 15,504 | 944 | 702 | 16,213 | 211 | 9,928
IG.19 | 5,520 | 2,641 | 220 | 27 | 2,669 | 269 | 2,062
IG.20 | 28,290 | 12,059 | 411 | 85 | 12,159 | 227 | 12,880
Grand Total | 429,523 | 283,731 | 9,455 | 5,440 | 290,626 | 1,766 | 86,147
Production Planning And Achievement Summary Sheet Feb-2026

## Slide 9
IG Section – Downtime Analysis
Total: 2,510 | 12 M/C
Critical Problems (High Impact Issues)
IG.20: Maximum Quantity Loss (12,880 units).
IG.19: Extreme Down Time (269 hours).
IG.17: High Down Time (263 hours).
IG.15: Severe Rework Issues (2,055 units).
IG.04: High Rework Volume (1,135 units).
IG.01: Critical In-Running Rejections (1,299 units).
Major Warning Points (High Concern)
IG.11: Combined high loss (9,928 units), Rework (944), and Rejections (702).
IG.18: High Quantity Loss (10,443 units) with Rejection (730) and Rework (899) concerns.
IG.01: High Overall Quantity Loss (8,497 units).
IG.04: High Overall Quantity Loss (8,727 units) and Rejections (602).
IG.13: Significant Rework (930) and Quantity Loss (7,521 units).
IG.15: High Quantity Loss (7,215 units) and Rejections (800).
Downtime Concerns: High hours observed on IG.11 (211h), IG.20 (227h), and IG.18 (159h).

## Slide 10
Focus on these areas to reduce Rejection and Rework:
Audit IG.15 & IG.01: Find the root cause of high rework and rejections on these specific machines.
First-Piece Approval: 100% verify the first part after any New Setting or Wheel Change.
Hourly Checks: Perform frequent checks on IG.04 & IG.15 to catch errors early.
Skill Training: Train operators on New Setting procedures to stop setup-related rework.
Wheel Maintenance: Ensure proper dressing and balancing for IG.16 & IG.04.
SOP Implementation: Use step-by-step "How-to" guides for settings to eliminate human error.
IG Section – Downtime Analysis
Total: 2,510 | 12 M/C

## Slide 11
IG Rework (ppm)
M/c2 | Sum of M/C Plan Qty. | Sum of Good | Sum of Rework
IG.01 | 60,997 | 48,836 | 649
IG.04 | 37,097 | 21,625 | 1,135
IG.12 | 21,474 | 13,855 | 704
IG.13 | 25,877 | 13,808 | 930
IG.14 | 62,622 | 49,901 | 693
IG.15 | 50,667 | 33,484 | 2,055
IG.16 | 52,484 | 42,431 | 277
IG.17 | 13,697 | 5,716 | 538
IG.18 | 38,763 | 23,871 | 899
IG.11 | 32,035 | 15,504 | 944
IG.19 | 5,520 | 2,641 | 220
IG.20 | 28,290 | 12,059 | 411
Grand Total | 429,523 | 283,731 | 9,455
Rework >= 1000 (Action Needed)
Rework 800 - 999 (Monitor)

## Slide 12
IG Rejection (ppm)
M/c2 | Sum of M/C Plan Qty. | Sum of Good | Sum of IN Running REJ.
IG.01 | 60,997 | 48,836 | 1,299
IG.04 | 37,097 | 21,625 | 602
IG.12 | 21,474 | 13,855 | 214
IG.13 | 25,877 | 13,808 | 257
IG.14 | 62,622 | 49,901 | 213
IG.15 | 50,667 | 33,484 | 800
IG.16 | 52,484 | 42,431 | 323
IG.17 | 13,697 | 5,716 | 188
IG.18 | 38,763 | 23,871 | 730
IG.11 | 32,035 | 15,504 | 702
IG.19 | 5,520 | 2,641 | 27
IG.20 | 28,290 | 12,059 | 85
Grand Total | 429,523 | 283,731 | 5,440
REJ >= 1000 (Action Needed)
REJ 500 - 999 (Monitor)

## Slide 13
📊 Per Person Output — Good Performance Analysis | Machine: IG.11 | February 2026
Sorted: Good Output ↑ (Lowest → Highest)
Date | Shift | Operator Name | Plan Hrs |  | TOTAL | GOOD | Rework | REJ
06-Feb | I | Pankajbhai Khasiya | 8 |  | 368 | 357 | 32 | 11
21-Feb | I | Vala Himesh | 8 |  | 436 | 410 | 49 | 26
17-Feb | I | Varshaben Mankoliya | 8 |  | 488 | 469 | 50 | 19
17-Feb | II | Hashmukh | 8 |  | 493 | 470 | 65 | 23
20-Feb | I | Vala Himesh | 8 |  | 528 | 517 | 45 | 11
18-Feb | II | Amit Makampara | 8 |  | 560 | 535 | 57 | 25
07-Feb | II | Pravin Baraiya | 8 |  | 611 | 555 | 42 | 56
16-Feb | I | Vala Himesh | 8 |  | 644 | 627 | 18 | 17
07-Feb | I | Himesh | 8 |  | 642 | 630 | 14 | 12
11-Feb | I | Varshaben Mankoliya | 8 |  | 670 | 670 | 0 | 0
09-Feb | II | Abhijitsinh Rana | 8 |  | 736 | 686 | 40 | 50
12-Feb | I | Pravin Baraiya | 8 |  | 779 | 718 | 27 | 61
19-Feb | II | Amit Makampara | 8 |  | 735 | 720 | 63 | 15
16-Feb | II | Hashmukh | 8 |  | 761 | 743 | 45 | 18
10-Feb | I | Varshaben Mankoliya | 8 |  | 795 | 755 | 39 | 40
08-Feb | I | Varshaben Mankoliya | 8 |  | 825 | 783 | 35 | 42
09-Feb | I | Varshaben Mankoliya | 8 |  | 873 | 813 | 60 | 60
06-Feb | II | Dilip Panday | 8 |  | 822 | 817 | 20 | 5
11-Feb | II | Taslimbhai Kondhiya | 8 |  | 925 | 900 | 18 | 25
10-Feb | II | Akash Kumar | 8 |  | 973 | 937 | 17 | 36

## Slide 14
FAILURE ANALYSIS REPORT: MACHINE IG.11
Excessive Downtime: Machine was down for approx. 4 hours due to mechanical breakdown and maintenance.
High Setup Time: Significant productive time lost in New Job Change and Trials at the start of the shift.
Poor Raw Material: 180 pieces rejected due to "Out of Spec" material quality, directly impacting output.
Higher Cycle Time: The specific job/part running that day had a longer production time per piece compared to other shifts.
Lower Machine Availability: Operator had only ~50% machine availability due to the combined impact of breakdown and setup.
Low Performance: Core Reasons
Date: 06-Feb-2026 | Shift: I (08:00 AM - 04:00 PM) | Operator: Pankajbhai Khasiya
Low Performance: Core Reasons
Factor | Pankajbhai (Bottom) | Akash/Taslimbhai (Top)
Machine Status | Major Breakdown | Smooth Running
Material | High Variation | Consistent Quality
Setup Time | ~1.5 Hours | 0 Hours
Actual Run Time | ~4.5 Hours | ~7.5 Hours
Summary Table: Pankaj bhai vs. High Performers

## Slide 15
OEE – IG Machines Avg.
Chart: OEE % per Machine
| IG.01 | IG.04 | IG.12 | IG.13 | IG.14 | IG.15 | IG.16 | IG.17 | IG.18 | IG.11 | IG.19 | IG.20
OEE % | 80.1 | 58.3 | 64.5 | 53.4 | 79.7 | 66.1 | 80.8 | 41.7 | 61.6 | 48.4 | 47.8 | 42.6
Chart: Rework & Rejection — Actual Quantity
| IG.01 | IG.04 | IG.12 | IG.13 | IG.14 | IG.15 | IG.16 | IG.17 | IG.18 | IG.11 | IG.19 | IG.20
Rework (Qty) | 649 | 1135 | 704 | 930 | 693 | 2055 | 277 | 538 | 899 | 944 | 220 | 411
Rejection (Qty) | 1299 | 602 | 214 | 257 | 213 | 800 | 323 | 188 | 730 | 702 | 27 | 85
Key Highlights
Best M/C (OEE)
IG.16 (81.8%) & IG.01 (80.1%)& IG.14(80)
Lowest / Worst M/C
IG.17 (41.7%) — needs attention
Highest Rework
IG.17 (538 / 9.1%), IG.19 (220 / 8.2%)
Highest Rejection
IG.11 (702 / 4.3%), IG.17 (188 / 3.2%)
Low Rework
IG.16 (277 / 0.6%), IG.01 (649 / 1.3%)
Low Rejection
IG.14 (213 / 0.4%), IG.20 (85 / 0.7%)
Fleet Avg OEE
60.4% vs 65% target
Fleet Avg Rework
3.3% (9,455 pcs)

## Slide 16
Key Insights & Recommended Actions
February 2026 – Management Action Summary
Critical Issues
Production achievement at 69% vs >95% target
IG Grinding rework - (36,256 ppm) exceeds
7,500 ppm target (4.8x )
IG Grinding rejection (21,361 ppm) exceeds
1,500 ppm target (14x )
EG rework (7,638 ppm) and rejection (1,939 ppm)
( both above targets )
Positive Highlights
FG rejection KPI met: 162 ppm vs 400 ppm target — excellent performance
Soft machining rejection : 4.98 ppm vs 150 ppm target
very low ( Rejection )
Turning rejection within target: 161.8 ppm vs 700 ppm
HO section: near-zero rejection, consistent OEE ~60%
Actions Plan
Priority: Deep-dive on IG.17 & IG.19 — root cause analysis for high rework (>8%)
Implement preventive maintenance for low OEE machines (EG.04, IG.17)
Review production planning — align capacity to achieve >95% target
Sustain FG and HO best practices; replicate across IG/EG machines